## Slide 1
EC-6701B-Service Manual

## Slide 2
Table of contents
一、Massage chair tools and use
二、Working principle of product circuit
三、Internal structure and disassembly of massage chair
四、Massage chair failure code

## Slide 3
一、Massage chair tools and use
1.tools

## Slide 4
2、Usage of multimeter
LED display
Data hold switch
Gear dial
Measuring port
Buzzer (diode test gear）
DC voltage Test gear V-
AC voltage test gear V~
Measuring port
HFE test socket
Resistance test gear Ω

## Slide 5
2.1、Test the function and function of the gear
Data hold switch：Memorize the measured data for comparison
Buzzer (diode test gear）：Measure the quality of diode, the on-off and alarm function of circuit
Resistance gear test gear：Measure the quality and value of resistance
DC voltage Test gear V-：Measure DC voltage
AC voltage test gear V~：Measure AC voltage
VΩ / COM：VΩ Red pen port (+ pole) during test, black pen port (- pole) during com test
Note: when carrying out resistance or voltage test, it is necessary to select a suitable range. If the range is too small to be measured, and the range is too large, the test error range is large; if the voltage is not known, it is necessary to select a range measurement with a large windlass.

## Slide 6
2.2、Measurement of line access/disconnection
Clear the way
Conducting
As shown in the left picture, first set the multimeter to the buzzer and power it
When the switch is on, the multimeter will display "0."; then contact the two probes with the ends of the red wire
At this time, the multimeter still shows "1." there is no change, which means there is an open circuit in the middle of the wire, that is, the line is open.
As shown in the picture on the left, if the multimeter shows the number of ". 002" or ". 00n" and gives an alarm, it means that the wire is connected.

## Slide 7
2.3、Measurement of AC voltage
As shown in the picture above: measure the household plug-in board power supply (220V), select the range of 750, and the test result shows "224", indicating that the actual voltage of this group of sockets is 224v at the moment (the switch is pressed down, so there is power, and the light is on).
As shown in the above picture: measure the power supply (220V) of our household plug-in board, select the range of 750, and the test result is displayed as "001", indicating that the actual voltage of this group of sockets is 0V at the moment (the switch is not pressed down, so there is no power, and the light is not on).

## Slide 8
2.4、Measurement of DC voltage
As shown above: test results are shown as” 1.58.””，The voltage of the battery is 1.58 V，And the red pen is connected to the battery“Positive” pole，The black pen is connected to the electromagnetic”ー” pole.
As shown above: the test results show”~ 1.58”, indicating that the battery has a voltage of 1.58 V on both ends, and the red pen is connected to the battery”~” Pole, black pen is connected to the electromagnetic“Positive” pole.

## Slide 9
J1（白）：蓝牙通讯
J2（黄）：接座下转接板J7（10-11）
J3（白）：接座下转接板J7（1-5）
J4（黑）：平板通讯
J5（黄）：中心盒上盖防夹
J8（白）：靠背推杆计数
J7（黑）：小腿推杆计数
J9（白）：接开关电源
J10（白）：电源输入
J14（白）：24V电源输出
J15（黑）靠背推杆
J16（红）：小腿推杆
J18（黄）：脚滚
J19（白）：接灵动可变推杆计数
J20（白）：座下3联气阀
J28（黑）：座下3联气阀
J22（红）：座下2联气阀
J23（红）：腰部加热
J25（蓝）：气泵
J27（绿）：灯带
二、Working principle of product circuit

## Slide 10
1、disassembly of the pillow：
1.unzip the zipper
2.remove the pillow
3.unzip the zipper
4.remove the big pillow
三、Internal structure and disassembly of massage chair

## Slide 11
2、disassembly of the backrest pad
1.unzip the zipper
2.unzip the zipper
3.unzip the zipper
4.unzip the zipper
5.disconnect the terminal
6.remove backrest pad

## Slide 12
3、disassembly of the legrest：
4、disassembly of main PCB：
1.Remove the DK gear card on both sides and move the calf to the right
2.disconnect the terminal and air hose
3.remove legrest
1.remove 4 screws
2remove 2 screws，disconnect the terminals
3.remove main PCB

## Slide 13
5、disassembly of the tablet：
1.Cut off the cable tie and disconnect the controller terminal
2.remove the tablet

## Slide 14
6、disassembly of the side panel：
1.unzip the zipper
2.Remove 2 screws and lift up the middle head cover
3.middle head cover unit
4.remove 4 screws
5.remove the rear cover
6.Dismantle two crossbeams

## Slide 15
6、disassembly of the side panel：
7.remove the screw both side
9.Disconnect the mating terminal
10.Disconnect the mating terminal
8.Disconnect the trachea and cut off the straps
11.Pry open the left side panel decorative strip
12.remove 2 screws

## Slide 16
6、disassembly of the side panel：
14.remove 2 screws
13.Pry open the right side panel decorative strip
15.remove 2 screws both side

## Slide 17
16.Lift up the left side panel
17.disconnect the air hose and terminals
18.remove left side pane
6、disassembly of the side panel：
19.Lift up the right side panel
20.disconnect the air hose and terminal
21.Remove the right side panel

## Slide 18
7、disassembly of the side seat：
1.remove 2 screws，disconnect air hose
2.remove side seat
3.Remove the cover and airbag

## Slide 19
8、disassembly of the inner side panel：
1.Remove 3 screws and pry open the side panel decorative strip
2.side panel decorative strip
3.Remove 3 screws and disassemble the side panel
4.Side panel separation

## Slide 20
1.Remove 2 screws and pry open the horn mesh cover
2.Remove 3 screws and dismantle the horn
3.the horn
4.Disassemble the horn mesh cover
5.Open the shoulder zipper and remove 2 screws
6.Remove the shoulder airbag
8、disassembly of the inner side panel：

## Slide 21
7.remove 5 screws
8.remove 4 screws，disconnect the terminals
9.remove Bluetooth PCB
11.triple valve
8、disassembly of the inner side panel：
10.Disconnect the air pipe and remove the 4 screws

## Slide 22
1.remove 2 screws（left side panel）
2.remove USB charging pcb
8、disassembly of the inner side panel：
4.triple valve
3.Disconnect the air pipe and remove the 4 screws

## Slide 23
1.unzip the zipper
2.remove arm cover
3.remove 2 screws，disconnect the air hose
4.remove air bag
5.remove the screw
6.remove remote control holder
8、disassembly of the inner side panel：

## Slide 24
1.remove 4 screws
2.remove the cover
3.Remove the USB socket decoration
8、disassembly of the inner side panel：

## Slide 25
4.remove 7 screws
5.Pry open the armrest cover
6.Remove the wireless charging unit
7.Remove the USB socket assembly
8、disassembly of the inner side panel：

## Slide 26
1.Side panel controller with upper cover component
2.Remove 3 screws and pry open the upper cover
3.Remove 5 screws
4.Side panel controller and armrest cover
8、disassembly of the inner side panel：

## Slide 27
9、Removal of movement connecting cord：
1.remove 4 screws，cut cable tie
2.Remove the ground screw and unplug the terminals
3.Remove the screws that fixing backrest cable
4.cut the cable tie，disconnect the terminals
5.remove backrest cable

## Slide 28
1.remove 2 screws，cut the cable tie
2.Pull out the 2 terminals on the movement board and remove the ground wire screws
4.Remove the baffles on both sides
4.screwdriver rotates the rolling motor, and the gear box moves upwards
5.remove upper gear box
10、disassembly of the upper gear box：
3.The walking motor has a slot, turn clockwise, and the movement moves down to the seat where the screws can be removed

## Slide 29
11、disassembly of the main PCB box：
1.Remove the cloth cover pin from the center box
2.remove 3 screws
3.disconnect the terminal
4.remove the main PCB box cover

## Slide 30
6.remove the screws fixing air pump box
7.remove 2 screws，disconnect the air hose and terminal
8.air pump
9.remove the screws fixing power PCB box
10.disconnect the terminal，remove 4 screws
11.power PCB
11、disassembly of the main PCB box：

## Slide 31
12、disassembly of the actuator：
1.Rollover massage chair
2.Disconnect the terminals and pull out the pins at the front and rear ends
3.Remove the inverted push rod
4.Remove the pins and screws and disassemble the adapter box cover
5.Pull off the flat push rod terminal
6.Remove the flat push rod

## Slide 32
7.Remove the front and rear pins and disconnect the terminal
8.Remove calf push rod
12、disassembly of the actuator：

## Slide 33
13、Internal disassembly instructions for the calf assembly：
1.Remove baffle
2.The baffle was removed
3.Unzip the zipper and remove the 3 screws
4.Unzip the zipper and remove the 3 screws
5.Break open the side plate shell and pull out the anti-pinch terminal
6.Break open the side plate shell and pull out the anti-pinch terminal

## Slide 34
7.Remove 4 screws
8.Remove 4 screws
9.Remove the calf drive plate
10.Remove the screws fixing the iron frame on the left
10.Remove the screws fixing the iron frame on the right
10.Remove the screws fixing the iron frame
13、Internal disassembly instructions for the calf assembly：

## Slide 35
11.Remove the air valve and kneading machine terminals
12.Pull out the trachea
13.Remove the screws holding the kneading machine
14.Remove the screws that secure the trachea
15.Separating kneading machine
15.Detach upper calf assembly
13、Internal disassembly instructions for the calf assembly：

## Slide 36
16.Lower calf includes upper calf iron frame
17.Cut off the tie buckle and remove 6 screws to remove the upper calf iron frame
18.Iron frame in lower calf
19.Remove 12 screws
20.Lower leg bottom cover
21.Cut off the tie buckle and remove 8 screws
13、Internal disassembly instructions for the calf assembly：
第页

## Slide 37
22.Pull out the trachea
23.lower leg separation
13、Internal disassembly instructions for the calf assembly：
第页

## Slide 38
4.Unzip the zipper and remove the screws holding the air bag
5.Pull off the airway terminal
6.Remove the air bag assembly
1.unzipped
2.Remove 2 screws
3.Lower calf holster
第页
13、Internal disassembly instructions for the calf assembly：

## Slide 39
7.Unplug the signal terminals and remove 12 screws
8.Foot machine components
第页
13、Internal disassembly instructions for the calf assembly：

## Slide 40
9.Remove 3 screws
10.Remove 1 screws
11.telescopic motor
第页
13、Internal disassembly instructions for the calf assembly：

## Slide 41
14、Removal instructions for underseat adapter plate：
1.Unzip the velvet zipper
2.Find the underseat adapter plate
3.Remove 2 screws
4.Remove 3 screws and pull out all terminals
5.Underseat adapter plate

## Slide 42
四、Massage chair failure code
fault number | fault description | Possible causes | elimination method | remarks
1 | The POWER button on the side panel is pressed for more than 40S | 1. There are key card keys | 1. Check the POWER key of the side panel | real-time detection
02 | The manual controller failed to communicate successfully with the center board for more than 4S | "1. Hand controller disconnected 2. Upper and lower limits are valid simultaneously before power-on " | 1. Connect the connection between the manual controller and the center board to the plug 2. Replace the manual controller connection 3. Check the upper and lower limit sensors and wiring " | real-time detection
03 | The upper movement control board and the center board failed to communicate successfully for more than 4S | 1. Poor contact between back frame and plug cord 2. Broken wire on back frame | 1. Poor contact between back frame and plug cord 2. Broken wire on back frame | real-time detection
04 | When the upper movement has a walking function on, abnormal walking count was detected | 1. Poor contact between back frame signal and patch cord 2. Travel counting sensor is broken | 1. Check whether the back frame signal pair plug cord is plugged in properly 2. Travel counting sensor is broken | real-time detection

## Slide 43
05 | Long press of side panel buttons exceeds 40S | 1. There are key card keys | 1. Check side panel buttons | real-time detection
06 | The center board manufacturing board and the calf board failed to communicate successfully over 4S | 1. Poor contact between the calf and the plug cord 2. The calf pair is inserted and disconnected | 1. Check whether the calf signal is plugged in properly 2. Replace the calf pair cord | real-time detection
07 | The kneading count of the upper movement is abnormal | 1. Abnormal movement kneading motor 2. Abnormal movement kneading drive circuit 3. The kneading counter board of the movement is abnormal | 1. Replace kneading motor 2. Replace the movement plate 3. Replace the kneading counter plate | real-time detection
08 | Abnormal knock count on upper movement | 1. Abnormal striking motor for movement 2. Abnormal movement knocking drive circuit 3. The movement strikes the counter board abnormally | 1. Replace the tapping motor 2. Replace the movement plate 3. Replace the knock counter board | real-time detection

## Slide 44
09 | The upper movement expansion count is abnormal | 1. Abnormal movement expansion motor 2. Abnormal movement expansion drive circuit 3. Abnormal movement telescopic counter board | 1. Replace the telescopic motor 2. Replace the movement plate 3. Replace the telescopic counter plate | real-time detection
10 | Upper movement heating sensor abnormal | 1. Abnormal movement heating drive circuit 2. Movement heating sensor abnormal 3. Movement heating sensor wire | 1. Replace the movement plate 2. Replace the movement heating swing arm 3. Replace the movement heating sensor cable | real-time detection
12 | Abnormal foot roller count | 1. Abnormal foot roller motor 2. The sole roller circuit is abnormal 3. The foot roller counting sensor is abnormal | 1. Replace the roller motor 2. Replace the calf plate 3. Replace the roller counter plate | Detection when entering self-test mode
17 | Lower calf extension counting signal is abnormal | 1. Lower calf extension motor is broken 2. Lower calf extension and counting line fell off 3. Lower calf extension counting sensor abnormal | 1. Replace the lower calf extension motor 2. Check the wiring of the calf extension motor 2. Replace the lower calf extension counting sensor | Detection when entering self-test mode

## Slide 45
19 | No counting signal detected when the calf push rod is turned on at 2.5S (Or the push rod in place signal is not detected in 40S) | 1. The calf push rod motor is broken 2. The calf push rod motor connection comes off | 1. Replace the calf push rod motor 2. Check the connection of the calf push rod motor | Detection when entering self-test mode
22 | The tablet POWER button is pressed for more than 40S | 1. There are key card keys | 1. Check the panel POWER button | real-time detection
25 | Back push rod opens 2.5S No count signal detected (Or the push rod in place signal is not detected in 40S) | 1. The backrest push rod motor is broken 2. The backrest push rod motor wiring comes off | 1. Replace backrest push rod motor 2. Check the backrest push rod motor wiring | Detection when entering self-test mode
33 | Lower calf extension and contraction upper and lower limits triggered simultaneously | 1. Lower calf extension upper and lower limit sensors are broken and the connection line falls off 2. Lower calf telescopic upper and lower limit sensor is broken | 1. Check the wiring of the upper and lower limit sensors in the lower calf 2. Replacement lower and upper limit sensors for lower calf are broken | Detection when entering self-test mode

## Slide 46
34 | Lower calf extension counting signal is abnormal | 1. Lower calf extension motor is broken 2. Lower calf extension and counting line fell off 3. Lower calf extension counting sensor abnormal | 1. Replace the lower calf extension motor 2. Check the wiring of the calf extension motor 2. Replace the lower calf extension counting sensor | Detection when entering self-test mode
35 | No front sensor signal detected in leg telescopic push rod 20S | 1. The telescopic sensor is broken or wiring problem 2. The telescopic motor is broken | 1. replace the sensor 2. Detection sensor wire 3. Replace the telescopic motor | Detection when self-test is turned on
36 | The leg telescopic push rod detects the front signal and detects the rear signal within 2.5S (the rear sensor is broken) | 1. The telescopic sensor is broken or wiring problem 2. The telescopic motor is broken | 1. replace the sensor 2. Detection sensor wire 3. Replace the telescopic motor | Detection when self-test is turned on
37 | No rear sensor signal detected by leg telescopic push rod 20S | 1. The telescopic sensor is broken or wiring problem 2. The telescopic motor is broken | 1. replace the sensor 2. Detection sensor wire 3. Replace the telescopic motor | Detection when self-test is turned on

## Slide 47
38 | The leg telescopic push rod detects the rear end signal and detects the front end signal within 2.5S (the rear end sensor is broken) | 1. The telescopic sensor is broken or wiring problem 2. The telescopic motor is broken | 1. replace the sensor 2. Detection sensor wire 3. Replace the telescopic motor | Detection when self-test is turned on
39 | Zero-gravity push rod is turned on for 2.5S and no counting signal is detected (Or the push rod in place signal is not detected in 40S) | 1. Zero-gravity push rod motor is broken 2. The zero-gravity push rod motor connection comes off | 1. Replace the zero-gravity push rod motor 2. Check the zero-gravity push rod motor wiring | Detection when entering self-test mode